## Slide 1
Interconnecting Enterprise Networks
Designing IP Addressing for Multi-Site Connectivity
DEPI Network Administration
Computer Networks

## Slide 2
Project Overview
Objectives
Scope
01
02
01
02

## Slide 3
Objectives
This project involves designing and documenting the network architecture of two interconnected enterprises .
The goal is to ensure efficient communication, redundancy, and scalability while implementing advanced services like DHCP, DNS, and dynamic routing protocols Connectivity .
01
02

## Slide 4
Scope
The network will connect two enterprises, each has its hierarchical model .
This involves reliable Layer 2 and Layer 3 connectivity within each enterprise and between the two
01
02
Technical Requirements

## Slide 5
Technical Requirements
OSPF
the IGP for routing within each enterprise
BGP
manage routing between the two enterprises
Management
VLAN segmentation for network management and security
Availability
Redundant multilayer switches (Active & standby)
DHCP
Dynamic IP Allocation
DNS
for applying Name Resolution
01
02
NETWORK TOPOLOGY

## Slide 6
NETWORK TOPOLOGY
Each enterprise's network topology follows a hierarchical model with:
Core Layer: 3 switches fully connected to each other, with one router handling external BGP connections to the second enterprise.
Distribution Layer: 2 multilayer switches (one active, one standby) connected the routers to handle VLAN traffic.
Access Layer: Each multilayer switch connects to the routers, managing the various VLANs for the departments.
Technical Requirements
IP Addressing Scheme

## Slide 7
IP Addressing Scheme
Enterprise 1:
  Network: 4 vlans AS 100
  Subnets:
    VLANs:
      VLAN 10 (Management): 10.10.10.0/24
      VLAN 20 (Users): 10.20.20.0/24
      VLAN 30 (Servers): 10.30.30.0/24
      VLAN 40 (DNS) : 10.40.40.0/24
  DHCP will be configured on the distribution layer (multilayer switch) to provide dynamic IPs in the range: 10.10.10.1/24 : 10.0.0.254/24
  Note That:(10.10.10.1,10.10.10.2,10.10.10.254) =>reserved
Enterprise 2:
  Network: 4 vlans AS 100
  Subnets:
    VLANs:
      VLAN 10 (Management): 10.10.10.0/24
      VLAN 20 (Users): 10.20.20.0/24
      VLAN 30 (Servers): 10.30.30.0/24
      VLAN 40 (DNS) : 10.40.40.0/24
  DHCP will be configured on the distribution layer (multilayer switch) to provide dynamic IPs in the range: 10.10.10.1/24 : 10.0.0.254/24
  Note That:(10.10.10.1,10.10.10.2,10.10.10.254) =>reserved
NETWORK TOPOLOGY

## Slide 8
IP Addressing Scheme
ROUTING PROTOCOLS
OSPF:
  OSPF automatically updates routing tables in response to network changes, such as the addition or failure of links. This ensures that data packets are always routed through the most efficient paths.
  OSPF supports a hierarchical network design using areas. This helps to manage larger networks by reducing the size of routing tables and minimizing the amount of routing information exchanged. The backbone area (Area 0) connects other areas, enhancing scalability and performance.
BGP:
  BGP facilitates routing between two separate enterprise networks, often referred to as Autonomous Systems (ASes). It enables seamless communication and data exchange between different organizational networks.
VLAN AND SEGMENTATION

## Slide 9
VLAN AND SEGMENTATION
VLAN 10:
Management traffic for routers and switches
VLAN 20:
Management traffic for routers and switches
VLAN 30:
….
VLAN 40:
…
01
02
NETWORK TOPOLOGY

## Slide 10
IP Addressing Scheme
Redundancy and Failover
Multilayer Switches:
  One multilayer switch is active, and the other is on standby for redundancy using HSRP (Hot Standby Router Protocol) .
Switches Redundancy:
  Routers are fully meshed to provide failover and load balancing .
VLAN AND SEGMENTATION
VLAN AND SEGMENTATION

## Slide 11
IP Addressing Scheme
Configurations
  CLICK ME
VLAN AND SEGMENTATION
VLAN AND SEGMENTATION
TESTING AND VALIDATION

## Slide 12
TESTING AND VALIDATION
Conclusion and Recommendations

## Slide 13
Conclusion and Recommendations
TESTING AND VALIDATION
  The designed network is optimized for scalability, redundancy, and efficient communication between the two enterprises. OSPF and BGP are configured to ensure smooth internal and external routing. Future recommendations include the deployment of additional security layers like an Intrusion Detection System (IDS) and upgrading bandwidth for potential growth.
U
O
K
N
A
H
T
Y

## Slide 14
U
O
K
N
A
H
T
Y